## Slide 1
START UP PAGE
Manual Cook Mode /
Recipe Creation
Press N Go / Favourites
Settings
All Recipes / Master Cookbook
Diagnostics

## Slide 2
Settings Examples
Entering setting would be PASSWORD protected
A 2 or 3 tier system may be required:
ENGINEERING
TECHNICIAN
STORE

## Slide 3
Single Timer Recipe Creation 1 of 2
RED “PLAY” button because no time has been entered
YELLOW “PLAY” button indicates that the unit will have to preheat before timer can start now that a higher temp has been entered
When CUSTOM prompt is selected, an TEXT EDIT icon appears allowing for the custom prompt to be created
Press icon to toggle between DONE, NONE and CUSTOM and then loop back to NONE if pressed again for Prompt Setting
DONE is default
Press “+” icon to add a stage or “-” to delete a stage
Press icon to switch to multi timer mode if desired
When second stage added is added, the default DONE prompt for stage 1 will automatically default to NONE and the default stage 2 prompt will be DONE

## Slide 4
Single Timer Recipe Creation 2 of 2
When finished press the green arrow
Select text box and use pop up keyboard to create the desired prompt text
Press icon create or edit the custom prompt
Press “>” icon to go to next stage
Press to save recipe
Press to start manual cooking
Toggle between the acknowledgment mode for the prompt: “finger icon” means the user must acknowledge the prompt to clear it from the screen; “timer icon” means the prompt will clear itself after a sett amount of time (amount of time can be changed in SETTINGS)

## Slide 5
Single Timer Recipe Cooking
Note unit turns OFF and goes back to home screen once all timers have expired and have bene acknowledged
The timer and graphic represent the TOTAL cook time (not just the stage time)
AN example of a SELF CLEARING custom prompt… there is no acknowledgement icon to press
If the STOP button is pressed during preheat, the grill will turn OFF and go to HOME screen
If the PAUSE button is pressed during a single timer recipe, the countdown timer will simply pause until the PLAY button is pressed; the YELLOW colour is used to visually signal that the timer is no longer counting down

## Slide 6
Probe Recipe Creation
Press icon to toggle to PROBE COOKING mode
Toggle between the acknowledgment mode for the prompt: MANUAL means the user must acknowledge the prompt to clear it from the screen; Self Clear means the prompt will clear itself after a settable amount of time
In this example, a second timed holding stage has been added to the recipe

## Slide 7
Probe Recipe Cooking
Note unit turns OFF and goes back to home screen once all timers have expired and have bene acknowledged
When probe cooking, the graphic represents delta to the desired probe temperature
AN example of a MANUAL acknowledgement custom prompt… the check mark must be pressed to clear this prompt (but all timers continue to work in the background)

## Slide 8
Multiple Timer Recipe Creation
RED “PLAY” button because no timers have been set (note this is not considered INFINITY MODE)
YELLOW “PLAY” button indicates that the unit will have to preheat before timer can start now that a higher temp has been entered
Press icon to go into Multi Tray mode
Go back to exit mode if desired
RED “PLAY” button because timer has not been set

## Slide 9
Multiple Timer Recipe Cooking
Pressing PAUSE would let you change temp or add/modify timers
Note unit turns OFF and goes back to home screen once all timers have expired and have bene acknowledged
Pressing PLAY after changes are made to resume

## Slide 10
Cooking with INFINITY Mode
Use the number pad and select “--:--” from keypad to use INFINITY mode
Usual default screen when manual cooking is selected
The grey graphic is used to show that there is no countdown underway
Press PLAY to preheat grill
Pressing PAUSE while in INFINITY mode will let you set a timer if you want… pressing PLAY without making a change will resume infinity mode as illustrated here

## Slide 11
Saving a Recipe
Press icon to go to saved photos to select an image for the recipe
Press SAVE
Press in text box and use keypad to enter a recipe name
Select a photo from the ones saved using <> to switch between pages of saved icons, or press the USB icon to upload a new image from a USB; Press checkmark when finished
Accept the recipe and save or select cancel if desired to exit
Return to screen where you can press PLAY and begin cooking

## Slide 12
Cooking using a previously SAVED recipe or FAVOURITE
Press “Press N Go” Icon
Select a recipe from the list of favourites and confirm choice
Note unit turns OFF and goes back to home screen once all timers have expired and have bene acknowledged

## Slide 13
Cooking using a previously SAVED recipe within the COOKBOOK
Press Cookbook icon to access all recipes that have been saved
Select a recipe from the list of favourites and confirm choice
Can use left and right arrows to change between pages and
Press green checkmark to start recipe